## Slide 1: Smart 3D Setup and Administration
Smart 3D 2018

## Slide 2: Know your instructor
Cherise Primm
  Over 7 years of experience working with Smart 3D
  Specialization in Setup and Administration, Interference Detection Service, Codeless IFC

## Slide 3: Prerequisites for this class
Experience with Microsoft Windows Operating System architecture
Experience with Microsoft SQL Server 2016 or Oracle 12c database server administration
Knowledge of 3D Plant Design CAD Concepts

## Slide 4: Agenda
Day 1
Introduction to Smart 3D (concepts, terminology)
System Setup
Project Hardware Sizing
Project Setup (Database Creation, permissions)
Day 2
Backup and Restore
Project Management (delete models, delete catalogs, hierarchy icons, create catalog)
Model Organization (Systems hierarchy)
Smart 3D Common Applications

## Slide 5: Agenda (Cont’d)
Day 3
Optimization for Roles
Set Default Colors
Model Data Reuse & Model Data Transform
Synchronize Model with Catalog
Database Maintenance
Database Integrity
Day 4
Error Logs and Memory monitor
Interference Checking Service
Point Cloud Reference
Reference 3D (R3D) Part I
Notes: Topics to add:
Model Data Transform (MDT)

## Slide 6: Agenda (Cont’d)
Day 5
Reference 3D (R3D) Part II
Intergraph Batch Services
Database conversion wizard (SQL ORACLE)
Database version upgrade

## Slide 7: Smart 3D Introduction

## Slide 8: Smart 3D - Database architecture
RDB
SCHEMA
RDB
MDB
CDB
SCHEMA
CDB
SDB
SCHEMA
SDB
Model Configuration
Site
Site Schema
Catalog
Catalog Schema
Model
Reports
Reports Schema

## Slide 9: Smart 3D - Database architecture
Site
Site Schema
Catalog
Catalog Schema
Model
Reports
Reports Schema
Model Configuration

## Slide 10: Smart 3D - Database architecture
Site database set:
Contains configuration and connection information and links the rest of the databases.
Catalog database set:
Contains the Reference Data used by all disciplines.
Store Design Modules (assemblies), Catalog Filters
Model database:
Contains and organizes all of the three-dimensional objects in the model, referenced objects data.
Stores definition and content of deliverables (Drawings and Reports), Model and user’s Filters, Styles, Surface Style Rules, etc.
Reports database set:
Optimize data retrieval from other five databases.
Model
database
Site database set
Catalog database set
Reports
database set
Model Configuration

## Slide 11: Smart 3D - Database architecture
Site 1
Model 1
Model 2
Model 3
Catalog 2
Report 3
Report 2
Report 1
Multiple Models can share the same Catalog …
Catalog 1
Model Configuration options
… or exclusively use own Catalog

## Slide 12: Smart 3D - Database architecture
Site 1
Model 1
Model 2
Model 3
Catalog 1
Catalog 2
Report 3
Report 2
Report 1
Model Configuration options
Multiple Model can share the same Catalog …
… or exclusively use own Catalog
Notes: 12

## Slide 13: Smart 3D intro: Server - Client architecture
Database Server
Interference Checking Server
Smart 3D Client
Smart 3D Client
Ancillary servers
Batch Server
- Name Generator
- SharedContent

## Slide 14: Smart 3D intro: Define Workspace
Filter on database
Returns only the data you want to see
and builds a logical “Working Set”
  System
  Assembly
  Spatial (Volume or Planes)
  Logical Permission Groups
  Object Types/Properties
Site Database set
Catalog Database set
Reports Database set
Model Database
Workspace

## Slide 15: Smart 3D intro: Modeling environment
Discipline oriented interface
Drawings and Reports
Graphic views
Main Menu
Task Toolbar
Active View
Status Bar
Common Toolbar
Workspace
Explorer
Active
command Ribbon bar
Access
Control
To Do list meter

## Slide 16: Smart 3D intro: Project Management
Create, backup and restore models
Modify user accesses to model objects
Start/Stop Interference checking
Configure Global Workshare
Migrate databases
Tree view
List view
Main Menu
Permissions
Hierarchy

## Slide 17: Smart 3D intro: Relationships and Integration
Smart 3D synchronizes key elements of integration and relationships.
Integration - Smart 3D allows multiple engineering disciplines to work concurrently and in real-time against relational databases.
Relationships - Smart 3D's relationship manager controls design changes across disciplines, which in turn establishes and maintains appropriate behaviors among structures, equipment, and systems.

## Slide 18: Smart 3D intro: Administrative guides
Smart 3D Release Bulletin
Smart 3D Installation Guide
Smart 3D Installation Checklist
Smart 3D Project Management User's Guide
Smart 3D Database Integrity Guide
Smart 3D Global Workshare Guide
Smart 3D Interference Checking Guide
Smart 3D Troubleshooting Guide
Smart 3D Point Cloud Guide

## Slide 19: System Setup

## Slide 22: System Setup: Smart 3D servers
One or multiple server machines can be used to provide the following required supporting services:
  Database server
    Provides hosting services for the Smart 3D databases
  Shared content file server
    Contains support files for the Smart 3D project, symbol definitions, drawing and reports templates, reference files, translator data, etc.
  Name Generator service provider
    Generates object names and contains naming rules for object placement and certain administrative functionality

## Slide 23: System Setup: Smart 3D ancillary servers
Ancillary servers are computers dedicated to perform a specific task with the purpose to offload processing from the main database server.
  Interference checking (IFC)
    Checks interferences between objects in the model
  Intergraph Batch services
    Manages scheduling and execution for commands to be processed in batch mode

## Slide 24: System Setup: Smart 3D workstation machines
Workstations connected to the database server
Administrative clients
  Used in administrative and maintenance tasks such as backups, restores, bulkload to catalog, database maintenance and integrity checks, attaching external references, manipulations with large data (MDR/MDT)
Modeling clients
  Contains all discipline related tasks and commands to create objects in a model
Output clients
  Contains all discipline related tasks and commands to create deliverables generated from model

## Slide 25: System Setup: Server - Workstation
Hardware recommendations
Supported platforms
Software prerequisites
Installation

## Slide 26: System Setup: Hardware recommendations Database server
  Intel Xeon® 5600 Series or better (64-bit instruction set, not Itanium®)
  32 GB to 128 GB or greater RAM depending on project size
  For hard drive size, see “Smart 3D Project Hardware Sizing Recommendations” in the Installation guide
  Backup system for server
  Access to DVD drive, either locally or through a network connection
  1 GbE or higher network interface for client connections, latency should be less than 1ms between client and database server

## Slide 27: System Setup: Supported platforms Database server
Supported Operating Systems
  Microsoft Windows Server 2016 (Standard or Enterprise)
  Oracle Linux 7 (Oracle database only)
Supported Database Servers
  Microsoft SQL Server 2016 (Standard edition for stand-alone environments; Enterprise edition for Global Workshare environments; 64-bit)
  Oracle 12c Release 2 (12.2.0.1) (Enterprise or Standard Edition 2; 64-bit)
    If you are going to use Oracle in a Global Workshare configuration, you also need Oracle GoldenGate 12.3.0.1.2, which is separately purchased from Oracle
  Oracle Linux 7 does not support a Global Workshare configuration

## Slide 28: System Setup: Software prerequisites Database server
Software prerequisites
  Adobe Reader or equivalent PDF reading software
  Microsoft XML Core Services (MSXML) 6.0 SP1 (Database server only)
  Microsoft .NET 4.6 or later

## Slide 29: System Setup: Installation of Smart 3D Reference Data – Name Generator
Reference Data
  Shared Content files
  Database Templates
  Oracle initialization scripts
Name Generator Service

## Slide 30: System Setup: Installation of Smart 3D Reference Data

## Slide 31: System Setup: Installation of Smart 3D Name Generator

## Slide 32: System Setup: Installation of Smart 3D Workstation
Applicable Hardware configurations
  Administrative Client workstation
  Modeling Client workstation
  Interference Detection computer/server
  Drawing Batch computer/server
  Name Generator computer
  Duplication and Synchronization computer
  Smart 3D Piping Specification Remote computer

## Slide 33: System Setup: Hardware recommendations Workstation
Intel Core i7, Quad Core
6+ GB RAM
Access to a DVD drive, either locally or through a network connection
Monitor capable of a minimum of 1280 x 1024 resolution
1 GbE or higher network interface
Graphics card designed for 3D intensive applications that meet the following requirements:
  32-bit main RGBA pixel buffer
  Hardware OpenGL 2.1 support
  Hardware Z buffer: 24 bit or higher
  256 MB RAM
  8-bit stencil buffer
  Hardware Alpha blending support
  Graphics acceleration set to full
  Hardware Anti-aliasing support recommended
  Latest available drivers should be installed

## Slide 34: System Setup: Supported platforms Workstation
Supported Operating Systems and required service packs
  Microsoft Windows 7 - Professional or Enterprise SP1 (64-bit)
  Microsoft Windows 10 (64-bit)
  Microsoft Windows Server 2016 (64-bit) Standard or Enterprise only as a client for Citrix XENApp 7.11
Supported database clients and required versions
  Microsoft SQL Server Management Studio 2016 or 2017 (64-bit)
  Microsoft SQL Server Native Client 2012 64-bit (11.3.6538.0 or later) (Required for all client computers when using Microsoft SQL Server databases)
  Oracle 12c R2 (12.2.0.1); 32-bit Oracle client only (Required for all client computers when using Oracle databases)
    NOTE: Oracle Instant client will not work

## Slide 35: System Setup: Software prerequisites Workstation
Software prerequisites
  Microsoft Edge Browser or Internet Explorer 11 or later
  Adobe Reader 11 or later (or equivalent PDF reader software)
  Microsoft XML Core Services (MSXML) 6.0 SP1
  Microsoft .NET Framework 4.6 or later
  Microsoft Office 2016
  SmartPlant License Manager 2012 (12.0.9) or later
Notes: 35

## Slide 36: System Setup: Optional software Workstation
Intergraph SmartPlant Schema Component 2018
  Allows publishing to SPF or 3D Model generation
Intergraph Batch Services 2010 SP1 (6.01.10.00)
  Allows scheduling commands for batch and/or remote processing
PDS Data Access components
  Allows referencing or export of PDS Projects
Solid Edge Version ST5 and ST10
  May be used for creating equipment symbols
Visual Basic 6.0 (Visual Studio 2013 or higher for .NET API)
  Allows creation of graphic visual basic symbols, macros, custom rules, etc.
Point Cloud vendor software
  Allows referencing Point Cloud projects in Smart 3D
Notes: 36

## Slide 37: System Setup: Installation of Smart 3D Design /Admin Client Installation

## Slide 38: System Setup: Installation of Smart 3D 64-bit Services
64-bit Services can be used for IFC service and/or Drawing Batch Services
These cannot be uninstalled individually. Need to uninstall Smart 3D software.

## Slide 39: Setup and Administration Lab
Lab 1

## Slide 40: Smart 3D Setup

## Slide 41: Smart 3D Setup
Software versioning is based on the different releases.
RTM - Release To Manufacturing (CD/DVD)
Service Packs or Schema Changes
HotFixes
Current version: Smart 3D 2018 (12.00.25.0004)

## Slide 42: Smart 3D Setup: Silent Install
Smart 3D can be installed through command line
Ideal to reduce deployment and maintenance impact
Service Packs or Hotfixes support silent install

## Slide 43: Smart 3D Setup: Silent Install
S3DInstallation.exe SERIALNUMBER=### SLAACCEPT=YES [INSTALLDIR=<Path>] [X64SERVICES=Yes] [ADDLOCAL=Feature1,Feature2] [REMOVE=Feature1,Feature2]

## Slide 44: Smart 3D Setup
Three different ways to configure Smart 3D.
Server
Name Generator
  Shared Content
Workstation
Project Management
Bulkload
IFC…
Standalone
Global Workshare Configuration

## Slide 45: Smart 3D Setup
Before Installing…
Use an account with administrative privileges
If installing under Windows 7, Windows 10 or Windows Server 2016, execute setup.exe with the option “Run as Administrator”
Verify that all prerequisite software was installed
Don't skip any restart recommended by the software

## Slide 46: Smart 3D Setup: Splash screen

## Slide 47: Smart 3D Setup
Reference Data installation

## Slide 48: System Setup: Installation of Smart 3D Reference Data
Notes: Provide User’s and Organization information
Read instruction, act accordingly
Optionally modify installation location (path)
Close Installation wizard (with option to review Smart 3D ReadMe document)

## Slide 49: Smart 3D Setup
Name Generator installation

## Slide 50: System Setup: Installation of Smart 3D Name Generator
Notes: Provide User’s and Organization information
Read instruction, act accordingly
Optionally modify installation location (path)
Enter account and password for Name Generator
Close Installation wizard (with option to review Smart 3D ReadMe document)

## Slide 51: Smart 3D Setup
Workstation Installation (Design and/or Admin Client)

## Slide 52: System Setup: Installation of Smart 3D Design Client Installation

## Slide 53: System Setup: Installation of Smart 3D Design /Admin Client Installation
Notes: Provide User’s and Organization information
Read instruction, act accordingly
Optionally modify installation location (path)
Close Installation wizard (with option to review Smart 3D ReadMe document)

## Slide 54: System Setup: Installation of Smart 3D Full Installation
Notes: Provide User’s and Organization information
Read instruction, act accordingly
Optionally modify installation location (path)
Close Installation wizard (with option to review Smart 3D ReadMe document)

## Slide 55: System Setup: Installation of Smart 3D Full Installation

## Slide 56: System Setup: Installation of Smart 3D Full Installation

## Slide 57: Smart 3D Setup: HotFix installation
Installed through a GUI with similar options to base installation.
Can be installed silently with a script.
HotFixes are listed as updates to Smart 3D in the list of programs.

## Slide 58: Smart 3D Setup: HotFix installation

## Slide 59: Smart 3D Setup: HotFix installation

## Slide 60: Smart 3D Setup: Configurations
Final Configurations for a Workstation
  Verify firewall is either turned off or proper exceptions have been set
  Register SQL Server on administrative computers or configure the Oracle Net service

## Slide 61: Smart 3D Setup: Configurations
Final Configurations for a Reference Data server
  Share to the network and adjust proper permissions on the Shared Content folder
Final Configurations for a Name Generator server
  Set proper exceptions in the Windows Firewall to allow inbound requests on port 8081

## Slide 62: Project Setup

## Slide 63: Project Setup: Hardware sizing recommendations
Hardware sizing, especially for servers, depends on many factors such as:
- The number of concurrent users per server
- The number of locations (Global Workshare)
- The size of the project (which translates into the size of the databases)
- Other software that is running on the machine
Notes: 63

## Slide 64: Project Setup: Hardware sizing recommendations
The users per server that define the different project sizes (small, medium, and large) need to be taken as an effective number. The effective number of users should be calculated by taking into consideration the following:
Drawing Batch server - add 3 users
Remote IFC - add 1 user
Global Workshare Setup - For each server add 25% of the total concurrent users of all the other servers.
Ef = Cu + (0.25 * (Ct))
Where:
Ef = effective concurrent users for one server
Cu = concurrent users for this server
Ct = total concurrent users for all other servers
Notes: 64

## Slide 65: Project Setup: Hardware sizing recommendations
Example:
In a Global Workshare project with 3 servers (locations), 40 users will connect to two servers, and 5 users will connect to one server:
Ef = Cu + (0.25 (Ct))
When all 3 servers are working concurrently, the equivalent number of users at each server is:
The equivalent number of users at each one of the 40-user servers are:
  40 + (0.25 * (45)) = 51.25 users
The equivalent number of users at the 5-user server is:
5 + (0.25 * (80)) = 25 users.
Cu= 40
Cu= 40
Cu= 5
Global Workshare
Notes: 65

## Slide 66: Project Setup: Hardware sizing recommendations
Project Size | Effective users on one server | Model database size | IFC Server | Batch Server
Small project | 1 to 15 | Up to 20 GB | Separate server or workstation | Separate server or workstation
Medium project | 16 to 50 | 20 - 50 GB | Separate server or workstation | One or more separate server or workstation
Large project | 51 to 100 | 50 GB or more | Separate server or workstation | Multiple separate servers or workstation
Notes: 66

## Slide 67: Project Setup: Hardware sizing recommendations
Project Size | Small | Medium | Large
Number of processor cores (one Core 2 Duo counts as two) | 4 | 4 - 8 | 8 or more
Memory for SQL Server 2014 and Oracle 12c | 32 GB | 64 GB | 128+ GB
Bus Size, OS, and Database | 64 bit | 64 bit | 64 bit
Notes: 67

## Slide 68: Project Setup: Familiarize with the software
Notes: Verify what is installed if everything is selected
68

## Slide 69: Project Setup: Database creation
Site and Catalog database creation
  Database Wizard
Model creation
  Project Management

## Slide 70: Project Setup: Create a model from scratch
Site
Database Wizard AppRepos.dat/dmp
Site Schema
Catalog Project Management AppRepos.dat/dmp
Database Wizard CatalogDB.dat/dmp
Catalog Schema
Model
Reports Project Management
Reports Schema

## Slide 71: Project Setup: Permissions hierarchy
Model/Catalog root
  Top level item in the hierarchy
Permission Group Folder
  A set used to organize permission groups
Permission Group
  Portion of model/catalog over which various people have various levels of access and responsibility

## Slide 72: Project Setup: Permissions hierarchy
This hierarchy is seen only in Project Management
Can have unlimited number of levels of folders
Cannot have permission groups and permission group folders at the same level
Permission Groups are the last leaf in a branch
Copy/Paste permission groups available

## Slide 73: Project Setup: Sample Permission Objects hierarchy

## Slide 74: Project Setup: Modify Permission Objects hierarchy
Rename command
Folders cannot be deleted if there are Permission Groups under them
Permission Groups containing objects cannot be deleted
Copy/Paste of Permission Groups and Folders copies just the Permission Objects, not model items contained within. Name has to be unique within container (catalog or model).
Move command allow to relocate Permission Objects within container

## Slide 75: Project Setup: Root vs Permission Group assignment
Permissions can be granted for Windows Security Object (Groups and/or Users) at the Model/Catalog Root and Permission Group level
Permissions granted at Model/Catalog Root level allow access to modify permissions hierarchy within the model and perform various administrative tasks.
Permissions granted at Permission Group level affect access to objects within that permission group. These are used for general modeling purposes.

## Slide 76: Project Setup: Association concept
When objects are placed, they will be automatically assigned to a permission group.
Objects can be associated to systems belonging to permission group where user has access
Objects can only be modified or deleted if user has access to permission group assigned to the object.
You can associate objects to those Work Breakdown Structure (WBS) items to which you have access based on the permission group they belong to.

## Slide 77: Project Setup: Permission access levels
Read = view objects
Write = create/modify/delete objects
Full Control = create/modify/delete + approve or reject objects

## Slide 78: Project Setup: Object status
Working
  Initial status of all objects; Objects can be edited/deleted while in this status
In Review
  Object is in read-only mode and waiting for approval/rejection
Rejected
  If an object is found to be incorrect, reviewer can send object to this status
Approved
  If an object is found to be correct, reviewer can send object to this status

## Slide 79: Project Setup: Status change based on permissions
Read
  can’t change status
Write
  can change from Working to InReview
  can change from InReview to Working
  can change from Rejected to Working
Full Control
  can change from any status to any status

## Slide 80: Project Setup: Permissions logical model
 | View | Create/Modify/ Delete | Send to review/ bring back | Approve/ reject
Read | Ö |  |  | 
Write | Ö | Ö | Ö | 
Full Control | Ö | Ö | Ö | Ö

## Slide 81: Project Setup: Add users to permission groups

## Slide 82: Project Setup: Remove users from permission groups
Select the users to be removed
Pick the places they need to be removed from

## Slide 83: Project Setup: Access Permissions for SQL
Administrator
  Sysadmin & Public (Server Roles)
  No user mapping
Designers
  Public (Server Roles)
  User Mapping: db_datareader, db_datawriter & mapping to all 7 Smart 3D databases for a project. The users will also need Execute permission to each database.

## Slide 84: Project Setup: Access Permissions for Oracle
Scripts delivered with Smart 3D Reference Data are located at [Product Folder]\ProjectMgmt\Tools\OracleScriptsToInitDB.
Scripts need to run in this order:
  Create Roles for Smart 3D Users
    SP3DUser_ROLES.SQL
    SP3DProjectAdministrator_ROLES.SQL
  Create Users for Smart 3D
    SP3DUser.SQL (for Oracle) or
    Linux_SP3DUser.SQL (for Linux)
  Create Administrative Users
    SP3DProjectAdministrator.SQL (for Oracle) or
    Linux_SP3DProjectAdministrator.SQL (for Linux)

## Slide 85: Project Setup: Minimum Access Privileges for Oracle
These script files create the necessary schemas, users, and roles that are used to run the software on Oracle with minimum access privileges
Scripts delivered with Smart 3D Reference Data are located at [Product Folder]\3DRefData\Tools\OracleScriptsToInitDB\MinimumAccessPrivileges
Scripts need to run in this order:
  Create Roles for Smart 3D Users
    SP3DUser_ROLES.SQL
    SP3DProjectAdministrator_ROLES.SQL
  Create Users for Smart 3D
    SP3DUser.SQL (for Oracle) or
    Linux_SP3DUser.SQL (for Linux)
  Create Administrative Users
    SP3DProjectAdministrator.SQL (for Oracle) or
    Linux_SP3DProjectAdministrator.SQL (for Linux)

## Slide 86: Database User Authentication: Why Support It?
Concern that OS authenticated users could connect outside of S3D with standard database tools (SQLPLUS, SQLCMD, SSMS) and cause damage. Other PPM products support DB user authentication.
A unified solution for S3D connecting to Oracle on Linux.
  First implementation was relying on Oracle Wallet.
OS authentication does not allow connection to a database from a not trusted domain.
  DB user authentication resolves the connection to database but Symbol share access problem remains.

## Slide 87: Database User Authentication
Database logins are accounts created in the database management system (i.e. SSMS). These accounts are separate from the login account you use to connect to the operating system
To open a connection to the database, a windows user has to type the user name and password every time.

## Slide 88: Database user login on SQL server
Make SQL server use mixed mode authentication (it is NOT set by default) using SQL server management studio “Server/Properties” page.
Create a database user login
Grant permission to that user on each database. Required roles for S3d standard user are:
    public,
    db_datareader,
    db_datawriter
    User must also have “Execute” (any stored procedure) permission on each database.

## Slide 89: Database user login on Oracle
Look for scripts under [INSTALLDIR]\ProjectMgmt\Tools\OracleScriptsToInitDB
For a standard user, open the script SP3DUser.sql
  replace “DOMAIN\USERNAME” with “TheUserName” (not case sensitive).
  Replace IDENTIFIED EXTERNALLY with IDENTIFIED BY [TheUserPassword]
Example:
  DROP USER S3dStandardUser CASCADE;
  CREATE USER S3dStandardUser PROFILE DEFAULT IDENTIFIED BY S3dUserPassword
  DEFAULT
  TABLESPACE USERS TEMPORARY
  TABLESPACE TEMP ACCOUNT UNLOCK;
  GRANT UNLIMITED TABLESPACE TO S3dStandardUser;
  GRANT SP3DUSER TO S3dStandardUser;
  COMMIT;

## Slide 90: Database authentication and S3D user Access control
Database User or OS authentication are not impacting S3D user access control.
S3D Permission groups are NOT based on database users.
  Permission group access are based on OS user logged on the workstation.
For an S3D object, “user creator” or “last user modifier” are the id of OS user logged on the workstation.
  On S3D V2014R1 or earlier, those columns were based on the database user login.
  To support Oracle Linux, a CR was implemented early on S3D V2016 to be based on user logged on the workstation.

## Slide 91: How S3D decides to use OS or DB authentication
S3d client connecting to the database.
Read from file:
ServerName
DBuserName
password (encrypted)
Read in registry location of file containing DB user info.
Open the connection.
Use OS authentication.
Not found?

## Slide 92: Database Admin Setup for Database User Authentication
The database administrator creates a database user login.
That database user login is granted permission on the databases for a model database.
  Site,Site_Schema,Catalog,Catalog_Schema,Model,Report,Report_Schema
The database administrator creates a DBAuthentication.ini file on a shared folder.
  DBA uses [InstallDir]\ProjectMgmt\Tools\bin\ConfigureDBLoginFile.exe to create that file.
  <DBAuthentication.ini> contains: ServerName, databaseUserName, encryptedDatabasePassword.
  Multiple servers can be in DBAuthentication.ini.
  A server name must be unique on a DBAuthentication.ini.

## Slide 93: Setup and Administration Lab
Labs 2 - 4

## Slide 94: Backup and Restore

## Slide 95: Backup and Restore: Overview
Backup
Project Management Backup
Manual backup of the Shared Content folder
Restore options
Restore one or more model databases from backup
Restore model for selective recovery of model objects
Restore model as a copy

## Slide 96: Backup and Restore: Project Management Backup
Model, Catalog and Site databases are backed up, reports databases are excluded.
A backup configuration file (bcf) containing information about the backup set is created in the location specified for the backup
Backup files will be saved to database server by default
Backups may be saved to a network location, additional configurations are required for this

## Slide 97: Backup and Restore: Project Management Backup
There are no individual files to be backed up – only complete databases
To complete the backup set, user needs to manually backup the Shared Content folder for the model
Multi-model backup available
User running the backup as well as account used as logon for Oracle Windows NT Service need to have write permissions on the folder under which backup files will be created.

## Slide 98: Backup and Restore: Project Management Backup

## Slide 99: Backup and Restore: Restore options

## Slide 100: Backup and Restore: Restore one or more model databases from backup
Restores previously backed up models overwriting the existing one.
You can only restore a complete model (no partial restore)
Catalog can be overwritten or not depending on user selection to prompts
Items that were manually backed up (Shared Content folder) need to be manually restored as well

## Slide 101: Backup and Restore: Restore model for selective recovery of model objects
Restores a model from a previous backup, without overwriting the existing model.
Allows for selective recovery of objects from previous versions of the same model without losing object identity or relationships
The restored project will exist in the Site database in parallel to the current project and would share the same catalog.

## Slide 102: Backup and Restore: Restore model as a copy
Allows the restore of models that were backed up from a different site database.
Allows to create a replica but independent model from the production model backup (test models).
Ability to change the name of the model and the restored model and catalog databases.
When the selected model to restore is registered with SmartPlant Foundation, the registration is removed from the copy during the restore.

## Slide 103: Backup and Restore: Off-site Restore
May be used to restore entire project on a new location, it can be due to a change in database servers, or to restore a backup received from a third party company.
  Using database wizard, restore site from backup set
  Using project management, restore model from backup (this brings in catalog associated with the model)
  Regenerate report databases
  Manually copy all the Shared Content files and outputs to the remote site
  Custom symbol dlls need to be registered on each client workstation at the remote site if required

## Slide 104: Setup and Administration Lab
Lab 5 – 8

## Slide 105: Project Management: Delete a Model
Full Control permission at the root level.
Option to drop or leave the physical database files in place.
For models in Oracle, the software may not delete all of the associated database objects. To delete schema information after deleting an Oracle model, you must use the Oracle Database Tools Wizard for Smart 3D located at [Product Directory]\ProjectMgmt\Tools\bin\SP3DOracleDBToolsWizard.exe.
Notes: 105

## Slide 106: Project Management: Delete a Catalog
Catalogs can only be deleted if they are not associated with any model.
In Oracle servers, Catalog must also be deleted using the Oracle Database Tools Wizard for Smart 3D
Notes: 106

## Slide 107: Project Management: Hierarchy Icons
Top level of the hierarchy
Reference data
Catalog associated with a model
Catalog associated with a model. Missing database
Catalog associated with a model. Needs to be upgraded
Catalog not associated with a model
Catalog not associated with a model. Missing database
Catalog not associated with a model. Needs to be upgraded
Model
Model missing database
Model needs to be upgraded
Permission group folder
Permission group
Notes: 107

## Slide 108: Project Management: New Catalog Command
Create a new empty catalog or create a catalog from a template.
Default permission groups and access rules are created.
In a Global Workshare configuration, the Database > New > Catalog command is available at the Host location, but not at the Satellite locations.
Every catalog must be associated to a Shared Content folder
Notes: 108

## Slide 109: Project Management: New Catalog Command
Notes: 109

## Slide 110: Custom Properties: Define Property Schema
Additional properties for models, permission group folders and permission groups can be added
Properties can be viewed in project management environment but are also reportable
Property information for models is stored in the site database to which they belong
Property information for permission folders and permission groups is stored in the model to which they belong
Notes: 110

## Slide 111: Custom Properties: Define model property
Notes: 111

## Slide 112: Setup and Administration Lab
Lab 9 – 11

## Slide 113: Model Organization (Systems)

## Slide 114: Systems and Specs: Contents
System hierarchy
Create and modify Systems hierarchy
Assign allowed specifications

## Slide 115: Systems and Specs: Systems overview
A system is a container that group objects logically
Systems have other systems as children creating a hierarchy with unlimited levels
Subsystems can belong to a different permission group from their parent
Many different types of systems are supplied (discipline specific and generic)
Every object must belong to a system
Different types of objects can be associated with different system types

## Slide 116: Systems and Specs: System types
Generic system
HVAC system
Equipment system
Pipeline system
Unit system
Conduit system
Electrical system
Piping system
Structural system
Area system

## Slide 117: Systems and Specs: Create and modify Systems hierarchy
Create new System commands
Copy and paste of Systems
Importing from excel

## Slide 118: Systems and Specs: Create new System commands
Creates a system as a child of the currently selected system
Currently active name rule for the system type being created is used to generate the name
If currently active name rule is ‘User-defined’, you can enter the name during creation
Systems and specifications task – Dedicated function

## Slide 119: Systems and Specs: Create new System commands
Systems can be created from workspace explorer hierarchy.
Systems and specifications task - Contextual menu

## Slide 120: Systems and Specs: Create new System commands
Systems can be created from workspace explorer hierarchy.
Graphical tasks

## Slide 121: Systems and Specs: Copy and paste of Systems
Systems can be copied in Systems and Specification task or in the Workspace Explorer
To select the entire hierarchy under a system, right-click the system then choose option “select nested”
Paste the hierarchy where desired (paste dialog box may appear)
You can copy and paste system hierarchies between two models that exists in the same site database

## Slide 122: Systems and Specs: Importing from excel
You can create an entire systems hierarchy or add pipelines to an existing hierarchy using an Excel workbook
Allowed specifications for pipelines can also be set in the workbook.
If specifications are allowed to pipelines in the workbook, these pipelines will not automatically inherit specifications allowed at parent levels including the root.

## Slide 123: Systems and Specs: Editing Systems
Deleting Systems
Renaming Systems
  User defined
  Default naming rule
Moving Systems
  Move using system’s properties page
  Move using drag and drop in the Systems and Specification task

## Slide 124: Systems and Specs: Allow specifications
Specifications limit part selection and placement based on rules.
By default, specifications are defined in the Catalog and must first be allowed to the Model
All systems inherit the specifications allowed at the Model root node, unless specifications were allowed from import command.
Each system must be allowed at least one specification

## Slide 125: Systems and Specs: Define allowed specifications
Systems and Specifications task

## Slide 126: Systems and Specs: Define allowed specifications
Whole categories can be selected with a single click
Notes: 126

## Slide 127: Systems and Specs: Define allowed specifications
Multi-selection of specifications and/or categories
Notes: 127

## Slide 128: Systems and Specs: Define allowed specifications
Multi-select of specifications from different categories
Notes: 128

## Slide 129: Systems and Specs: Define allowed specifications
Easier method to remove allowable specifications from a system
Switch to the specifications tab while browsing the systems hierarchy
Multi-select specifications and press delete button from ribbon bar
Notes: 129
In the systems and specs environment, rename command should be available on the right-click menu in the tree view and on the Edit menu.
Allow multi-select of systems in the tree view for copy/paste & delete

## Slide 130: Setup and Administration Lab
Lab 12 - 15
Notes: 130

## Slide 131: Common Applications

## Slide 132: Optimization for Roles

## Slide 133: Optimization for Roles
Used to refine Workspace definition filter
Roles are defined in delivered OptimizationforRole.xml
Location: \\Server\SharedContent\Xml
Each role is defined with a set of disciplines and subclass object types

## Slide 134: Default Color Configuration

## Slide 135: Default Color Configuration – The basics
Project Management command
  Import
  Export
  Configure Default Colors
  Apply Default Colors

## Slide 136: Default Color Configuration
Import
Aids in importing a set of “Default Style” rules into a model database
Used for porting rules from one model to another
Intergraph Defaults are available in SharedContent/XML folder

## Slide 137: Default Color Configuration
Export
Aids in exporting the “Default Style” rules from a model to be ported to another model

## Slide 138: Default Color Configuration
Configure Default Colors
Styles (colors) are applied per object type
Rules define the style applied to object types
Granular level of coloring based on object properties
Color by Role makes it possible to define different colors for same object type based on role (workspace simplification role) of the person using it.

## Slide 139: Default Color Configuration
Configure Default Colors

## Slide 140: Default Color Configuration
Configure Default Colors
Create a rule

## Slide 141: Default Color Configuration
Configure Default Colors
Create a rule

## Slide 142: Default Color Configuration
Configure Default Colors
Define criteria

## Slide 143: Default Color Configuration
Apply Default Colors
New Default Color Rules are applied to new or modified objects automatically
Apply Default Colors to change appearance of existing objects in the model
This is a time consuming process and shall be sparsely used

## Slide 144: Default Color Configuration
Considerations
New rules are automatically applied only to new or modified objects
Colors by default symbology rules are applied only to the simple physical aspect
Default colors may be used for colors such as object type or fluid code which are not expected to change through the life of the project, SSRs should be used for setting colors based on properties which change as project progresses such as approval status
Default colors are applied by default to insulation (translucent white), maintenance and operation aspects (translucent red) but SSRs may be used to apply other colors to aspects
Avoid testing on production models, time to apply default colors can impact testing time - use a model which has one occurrence of each object type for ease of testing

## Slide 145: Default Color Configuration
Considerations
Colors are not consistently applied on session files created prior to applying changes. New session files are recommended after making new rules.
When using default colors by Role, the colors will not be dynamically updated for saved sessions. New session files need to be created.
Colors will not change automatically to Intergraph's new color scheme after a version upgrade of existing models before V2014 R1, however new models created with 2018 will automatically apply the DefaultSymbologyRules.xml file from SharedContent/Xml folder.
Coloring equipment by classification will take care of equipment, components and shapes but for nozzles, edges available on Smart Support may need to be used to select nozzles with specific classification and apply default colors to them.

## Slide 146: Default Color Configuration
Considerations
Colors with the ‘Default’ role are automatically applied to SPR session exported from the S3D session, further overrides may be applied using property page for 3D Model Data or ReportSettings.txt for SPR Direct

## Slide 147: Setup and Administration Lab
Lab 16 - 18
Notes: 147

## Slide 148: Model Data Reuse (MDR)
Notes: 148

## Slide 149: Model Data Reuse: Introduction
Model Data Reuse (MDR) is a way to copy large amounts of 3D model data in a robust, scalable and intelligent way
MDR supplements the current copy/paste process – the existing process remains in place for smaller sets of data

## Slide 150: Model Data Reuse: Results

## Slide 151: Model Data Reuse: Advantages
MDR runs from Project Management environment as a wizard
  Interaction with objects is not required
Does not require objects to be loaded into memory
  process is scalable and can copy much larger sets of data
Software breaks down copy set into multiple transactions
  Process is robust and can tolerate a failure; it will continue to copy the rest of the remaining objects

## Slide 152: Model Data Reuse: Advantages
Software determines the sequence in which to copy objects
Permission group mapping to existing or default permission group
Transformation can be chosen using coordinate systems
Very good logging of process (including failures)
Copy of model objects between models is supported
Target locations in different servers is supported
Re-startable process

## Slide 153: Model Data Reuse: Recommended Practices
In Plant models, copying an entire unit system or area system. A unit or area typically includes many structural members, slabs, walls, equipment, foundations, pipe runs, ducts, cable trays, conduits, and hangers.
In Marine models, copying major sections of marine structure and outfitting. The sections may be organized into assemblies or blocks.
In Material Handling models, copying an entire conveyor system, including belts, equipment, modules, chutes, trusses, and trestles.

## Slide 154: Model Data Reuse
MDR command exists only in Project Management

## Slide 155: Model Data Reuse Workflow
Begin Model Data Reuse
Select source objects based on systems
Select disciplines to be copied (optionally WBS, Assemblies, Volume, Drawings)
Select a transformation
Confirm copy and review results
Select source objects based on filters
Select destination model and system (optionally map PGs)
Restart an Operation
Start a New Operation

## Slide 156: Model Data Reuse
The Model Data Reuse command invokes a wizard which allows you to complete the copy operation

## Slide 157: Model Data Reuse: Restart Operation
If the restart operation is selected then the user gets a list of all operations and their status.
Possible statuses:
  Stopped: Process terminated in an orderly way (User clicked stop on the progress button).
  Incomplete: Process terminated abnormally (Hardware/Software failure on client machine).
  In Progress: Operation is restarted on a different client machine.
  Completed: Operation completed successfully.

## Slide 158: Setup and Administration Lab
Lab 19 - 21
Notes: 158

## Slide 159: Model Data Transform
Model Data Transform (MDT) command allows you to move and/or rotate a large portion of the design objects in a model from one location in the model to another.
The processing is done in two phases:
  The first phase, the objects in each partition are disconnected from the surrounding objects.
  The second phase, the disconnected objects in each partition are transformed to their new location.
The set of objects can include read-only objects. If a read-only object prevents disconnection or transformation, MDT allows you to correct the situation and restart the operation.

## Slide 160: Model Data Transform : Best Practices
Create a backup
Disconnect objects at the boundary
Have write permission
Avoid concurrent editing
Model Data Reuse (MDR) and Model Data Transform (MDT) workflow using delete optional

## Slide 161: Model Data Transform : Best Practices

## Slide 162: Setup and Administration Lab
Lab 22
Notes: 162

## Slide 163: Synchronization

## Slide 164: Synchronize Model with Catalog
Used to propagate changes from the catalog to the model (including property, specification, and symbol changes)
CDB
MDB

## Slide 165: Synchronize Model with Catalog
The model database is updated to include the following changes:
Modifications to properties that have been bulkloaded into the catalog.
Modifications to name rules.
Parts that have been deleted from the Catalog are added to the To Do List.
Does not automatically synchronize Reference 3D models. You can choose to synchronize the Smart 3D model with the Reference 3D model when you update the Reference 3D project.

## Slide 166: Synchronize Model with Catalog
Actions performed by the Synchronization command will depend on the level of access of the user running the command from Project Management:
User with write access to model objects:
  Extended execution time
  Model objects will be updated automatically with no user interaction
User with read access to model objects:
  Reduced execution time
  Objects will not be updated automatically

## Slide 167: Synchronize Model with Catalog

## Slide 168: Synchronize Model with Catalog
To list all objects that have been flagged for interactive update in the model workspace, run Diagnostic Synch Workspace Report

## Slide 169: Database Maintenance Command

## Slide 170: Database Maintenance Command
Provides a tool to purge temporary data that may cause performance issues.

## Slide 171: Database Maintenance Command
Delete temporary symbol variations (flavors) in database
  These are temporary symbol variations that the software used during creation or placement of certain symbols.
Delete records of objects that users have deleted from model
Rebuild selected indexes
Reorganize selected indexes

## Slide 172: Setup and Administration Lab
Lab 23 - 25
Notes: 172

## Slide 173: Database Integrity

## Slide 174: Database Integrity: Overview
Database integrity problems are issues of the modeled objects that can in some circumstances prevent modeling activities or impact the accuracy of deliverables such as drawings or reports.
A typical example of a database integrity issue is an object that exists without a mandatory relation to another object in the model.

## Slide 175: Database Integrity: Overview
Important
These errors are not expected. However, in the event that they occur, you can correct them by perfoming the database integrity workflow in which objects will be addressed
We strongly recommend that you check the databases from time to time and promptly report any unknown problems to Intergraph.
If you receive a database integrity error that is not listed in documentation, contact Intergraph Process, Power & Marine Support.

## Slide 176: Database Integrity: Workflow
The workflow to address database integrity issues have three overall steps:
    1. Execute database integrity from Project Management.
    2. Generate a report to review issues found.
    3. Run Clean database command to address problems.

## Slide 177: Database Integrity: Execute Database Integrity
Execute database integrity from Project Management
  Check Database Integrity runs directly on a database (Site, Catalog, or Model), and creates records for the objects that need to be cleaned. Once the database has been scanned for errors, you can generate a report to review the errors that the Check Database Integrity command generated.
  You can run this command multiple times:
  To check the database for objects with integrity problems
  To confirm that objects have been deleted or cleaned (second pass)

## Slide 178: Database Integrity: Generate reports
Generate a report to review issues found
The software includes various report templates intended for diagnosing database integrity issues. You can run these report templates by opening a session in the software and clicking Run Report command from the Tools menu. Report templates are located in the Catalog Reports tab then under Report > Types of Reports > Diagnostics node. Select any of the four following reports:
Diagnostic clean database issues
Diagnostic clean database issues grouped by problem description
Diagnostic clean database issues grouped by status
Diagnostic clean database issues with column filters

## Slide 179: Database Integrity: Generate reports
  DataStore Displays whether the problem exists in the model or Catalog database.
  Problem Description Provides a brief explanation of the issue. Use it to search more details in DBIntegrity.pdf guide
  Status Determines if the issue is new, existing or resolved
  Severity Fatal, Crucial, High, or Normal
  Action to Take Describes what to do to fix the problem. Possible values include No Action, To Be Removed or To Be Repaired.
    If the action is To Be Repaired, you should run Clean Database custom command.

## Slide 180: Database Integrity: Run clean database command
Run Clean database command to address problems.
Consult latest DBIntegrity.pdf document for the correct workflow to fix the problem.
Most workflows involve use of the Clean Database custom command
  Action to take = To Be Repaired

## Slide 181: Database Integrity: Run clean database command
Clean Database Custom Command
SP3DCleanDatabaseCmd.CCheckObj

## Slide 182: Setup and Administration Lab
Lab 25
Notes: 182

## Slide 183: Error Log and Memory Monitor

## Slide 184: Error Log & Memory Monitor
Error Log
  On by default, but needs to be set for persistence (cleared when session closes)
  .Activate using …\Core\Tools\Administrator\Bin\ErrorLogEnable.exe
  4 Severity levels
  Time-based log file names
  Error log created per session or instance
Memory monitor
  Reports memory usage for all active Smart 3D sessions
  Different reporting states (Warning, Critical)
Notes: 184

## Slide 185: Error Log & Memory Monitor

## Slide 186: Error Log & Memory Monitor

## Slide 187: Troubleshooting Assistant
Consolidates error logging across all S3D tasks
Includes general S3D error logging (S3D error log, Assoc log)
Easy-to-use GUI
Ability to collect relevant files in zipped folder
Links to troubleshooting reference guide and Smart Support website
Download from Smart Support (smartsupport.intergraph.com)
  View Downloads > Smart 3D > Freeware Tools and Utilities > Uncertified Tools

## Slide 188: Troubleshooting Assistant

## Slide 189: Setup and Administration Lab
Lab 26

## Slide 190: Interference Checking (IFC)

## Slide 191: Interference Checking Detection (IFC): Overview
  Smart 3D provides two methods for IFC operation:
  Server-based Interference checking (database detection).
  - Runs on a separate server as a Windows NT Service
  - Looks for all interferences in the model
  Interactive interference checking (local detection).
  - Helps the designer in real time
  - Results are scoped to objects in a session (what you see in your workspace)

## Slide 192: IFC: Characteristics
Database Detect | Local Detect
Runs continuously (System Administrator choice) | Works only within the current session
Dedicated server minimizes impact on users and improves performance | Provides immediate graphical feedback (works immediately after commit)
Creates persistent interferences that are stored in the model database | Creates temporary interference markers in a user session
Based on administrator settings (controlled by permission groups) | Based on individual user settings
Provides feed back on how much has been checked | Checks only created and modified items

## Slide 193: IFC: Visual differences
Any interference detected by the server based detection method appear as a sphere
Interferences detected by local based detection method appear as a box

## Slide 194: IFC: Visual differences
Hard clash
Soft clash
Clearance clash

## Slide 195: IFC: Aspects
Aspect: Geometric area or space related to an object, such as its physical shape or the space required around the object.
Aspects are defined when a part class is created for the reference data.
Aspects can represent clearances for safety or maintenance areas.

## Slide 196: IFC: Aspects
Simple Physical
Detailed Physical
Insulation
Operation
Maintenance
Reference Geometry
Centerline

## Slide 197: IFC: Configuration

## Slide 198: IFC: Configuration – checking priority
Three types of checking priorities (based on object aspects):
Required - Produces a Hard type of clash
Optional - Produces a Soft type of clash
Not Checked - Elements currently displayed in this aspect will not be checked for interferences

## Slide 199: IFC: Configuration – comparison criteria
IFC can process the following combination of objects based on their checking priorities:
  Required – Required (Hard – Hard)
  Required – Optional (Hard – Soft)
  Optional – Optional (Soft – Soft)

## Slide 200: IFC: Configuration – Clearance rule
Clearance rules define the minimum distance between any two objects

## Slide 201: IFC: Configuration – Clearance rule

## Slide 202: IFC: Configuration – Permission group
All markers representing clashes or clearances will be assigned to a permission group

## Slide 203: IFC: Local detection
IFC local detection is available from all tasks in a session (Tools  Check Interference)
Very simple and intuitive GUI
Ribbon bar includes:
  Settings
  Visualization
  Review & approval commands

## Slide 204: IFC: Local detection
Local detection toolbar
Settings
Hide Interferences
Fit on Interferences
Show Interf.
List view
Close Toolbar
Refresh R3D Interferences

## Slide 205: IFC: Local detection

## Slide 206: IFC: Local detection – List view
Show interferences currently displayed in the workspace
Updates automatically
Sort by any column

## Slide 207: IFC: Database detection
Verify permission requirements (one time)
Configure interference service properties
Start interference detection Windows NT Service
Create IFC permission group folder and permission group (one time)
Start database interference detection process

## Slide 208: IFC: Database detection
Verify permission requirements (one time)
For the interference database detection process to run correctly, user setting up IFC must meet permission requirements according to the following guidelines:
Smart 3D user permissions:
  Full Control access at the root of the model is required to start/stop IFC Process
  Write access or higher to the designated IFC permission group
IFC Windows NT Service login permissions:
  Identity for the service must be a domain account that has Write or higher level of access to the designated permission group for IFC. If possible use login with a password not required to change as often as a corporate user account.
  User needs at least Read access on SharedContent folder
  User needs database access and permissions as a regular user to SQL or Oracle

## Slide 209: IFC: Database detection
Configure interference service properties

## Slide 210: IFC: Database detection
Start interference detection Windows Service

## Slide 211: IFC: Database detection
Create IFC permission group folder and permission group (one time)

## Slide 212: IFC: Database detection
Start database interference detection process

## Slide 213: IFC: Database detect
Modifications to Database Interference properties
If any change to settings on IFC properties form is to be done at any time during the life of the project, all objects in the model need to be reprocessed from the beginning (0% to 100%).
Notes: 213

## Slide 214: IFC: Codeless IFC
Codeless IFC is an Interference rule which is customizable using an XML configuration file, instead of code changes.
This functionality allows, using simple text based rules, to:
  Ignore objects for clash checking
  Ignore clashes between objects
  Set clash properties
With S3D 2016, it is delivered with the product.

## Slide 215: Setup and Administration Lab
Lab 27

## Slide 216: Point Cloud Model Reference

## Slide 217: Point Cloud Reference

## Slide 218: Point Cloud Reference
Smart 3D provides vendor-neutral point cloud data integration within the Model modeling software environment.
Saves redrawing an object, while still being able to add to it or build on top of it.
Point cloud models can be registered (attached) at the satellite location.
You can now move or rotate the attached point cloud in Project Management.

## Slide 219: Point Cloud Reference: Supported point cloud vendors
Leica Geosystems
Quantapoint
Trimble
Z+F UK

## Slide 220: Point cloud reference: Possible actions
Accessing Point Cloud (Accessories menu, filters)
Selecting a Data Point
Measuring
Interference Checking (IFC)

## Slide 221: Point cloud reference: Attach Point Cloud to model
Right click the model in Project Management
Select New Point Cloud Model Reference.
Select a vendor from the Select Point Cloud vendor to use list.

## Slide 222: Point cloud reference: Detach Point Cloud from model
Right click the model in Project Management
Select New Point Cloud Model Reference
Select None from the list of vendors to use

## Slide 223: Reference 3D (R3D)

## Slide 224: Reference 3D: Overview
Reference 3D (R3D) functionality facilitates the attachment of external 3D data as a reference model.
Such external data might have been published from another Smart 3D model or from a third-party model such as PDMS.
The data from external models is expected as a set of graphic (.zvf) and data (.xml or .drv) files.

## Slide 225: Reference 3D: Concept
.ZVF
.XML

## Slide 226: Reference 3D: Functionality
With Reference 3D you can do the following:
  Attach and orient (position, rotate, and scale) the reference model relative to the active model so that you can view the R3D data graphically and model against it.
  Control (add) R3D objects, hierarchy, and properties with user-defined schema and mapping files to extend the delivered R3D schema.
  Inspect the R3D model objects' properties and view their names through ToolTips.
  Use a powerful Smart 3D filtering mechanism on R3D Objects to filter objects from Reference 3D Models based on their type—regardless of the authoring tool used for creation (SP3D, SM3D PDMS, and so on).
  Extract simple General Arrangement drawings showing relative positioning of objects from R3D models, with limited annotation.

## Slide 227: Reference 3D: Transformation overview
O
E
N
200 m
150 m
90°
100 m
-125 m

## Slide 228: Reference 3D: Attaching Smart3D Models
.ZVF
.XML
Source Model
Publish Data
Attach as R3D Model
Target Model

## Slide 229: Reference 3D: Attaching PDMS Models
.RVM
.ATT
PDMS
Export RVM
.ZVF
.DRV
Translate Data
Attach as R3D Model
Smart 3D

## Slide 230: Reference 3D: Filters
R3D includes a very powerful filtering mechanism that allows you to filter objects from references based on their type, regardless of the authoring tool used for creation (Smart 3D, PDMS, and so on).

## Slide 231: Reference 3D: Business cases
Some of the business cases provided by this functionality include:
  Supporting disconnected workshare
  Preserving intellectual property in joint venture projects
  Allowing for better security in joint venture projects
  Compatibility between datasets from different S3D versions
  Bridging differences between Smart 3D datasets on disparate databases (Oracle vs SQL)
  Ability to work with datasets from external tools such as PDMS, XMpLant
  Support parallel design for increased productivity

## Slide 232: Reference 3D: Business cases
Some of the business cases provided by this functionality include:
Supporting Disconnected Workshare
Since the data is published to files at the source location(s) and attached as a reference at the target location, live connection between the databases is not required.
Periodic publish and update of the R3D models would allow multiple partners to work on a joint venture product in a disconnected manner.

## Slide 233: Reference 3D: Business cases – disconnected workshare
Sub Contractor
(Source Model)
Publish
Update
Prime Contractor
(Target Model)
Attach

## Slide 234: Reference 3D: Business cases
Some of the business cases provided by this functionality include:
  Supporting Parallel Design for Increased Productivity
If a project has many similar units, only one unit may be modeled and published. This published unit can then be attached multiple times with the required positioning.
Additional modeling such as civil work can be performed simultaneously
Model Data Reuse functionality can be used to actually replicate unit across to obtain real S3D objects

## Slide 235: Setup and Administration Lab
Lab 28 - 31

## Slide 236: Reference 3D: SPRDirect Output
Allows to publish Smart 3D reference objects (DGN/DWG, PDS) to Graphic (VUE) and label data (MDB2) files
Files can be opened in SmartPlant Review or using Reference 3D.
Easier and Faster way to get Smart 3D project to SPR where you can interactively review and analyze 3D model data.

## Slide 237: Reference 3D: Attaching SPRDirect Data
.VUE
.MDB2
SPRDirect Output
.ZVF
.MDB2
Translate Data
Attach as R3D Model

## Slide 238: Reference 3D: Convert to ZVF
ConvertToZVF.exe utility is delivered out of the box and can be found at the following location;
..\Core\Tools\Administrator\Bin\

## Slide 239: Reference 3D: Create Folder Hierarchy
If there is folder hierarchy on disk below the root folder of the R3D attachment, this folder hierarchy is automatically reflected in the WSE without having to do anything extra in S3D
Hide and show command works at any level in this hierarchy in WSE to quickly hide and show the graphics in that branch

## Slide 240: Reference 3D: Levels and Layers
The properties page of the R3D model, folder or file shows the levels or layers and display can be turned on or off using check boxes.
Surface style rules can be created based on Levels and Layers in the R3D model which can be exported to SP Review.
Filters can be defined based on Levels and Layers.
Surface style rules can be created based on these filters which can be exported to SP Review.

## Slide 241: Setup and Administration Lab
Lab 32

## Slide 242: Intergraph Batch Services

## Slide 243: Batch Services
This functionality allows scheduling of regular, time consuming tasks through the Intergraph Batch Services application.
  Database Integrity Command
  Backup Command
  Restore Command
  Structural import
  Structural export
  Drawings and Reports update
  Printing drawings
  Updating multiple R3D models

## Slide 244: Setup and Administration Lab
Lab 35 - 37

## Slide 245: Database conversion (SQL  ORACLE)

## Slide 246: Database Conversion Wizard : Overview
Used to convert databases from SQL Oracle
Prerequisites:
- SQL and Oracle databases should be running.
- Client machine needs SQL server registered and TNSNames entry for Oracle instance.
- Non-replicated databases.

## Slide 247: Database Conversion Wizard

## Slide 248: Database Conversion Wizard

## Slide 249: Schema Name Validator : Overview
The Schema Name Validator tool identifies names which are prone to fail due to Oracle 30 character limitation from site, catalog and model databases and dumps the data into an excel work book with type of data as work sheets.
This utility identifies part classes, custom interfaces, and custom interface attributes that violate the Oracle character limitation. This allows you to bulk load the data into an Oracle database, as long as the changes are updated in the bulkload data files.
This is particularly useful when converting MSSQL databases to Oracle databases.
This utility is delivered by default to the SchemaNameValidator.exe file in the <Product Folder>\Core\Container\Bin\Assemblies\Release\ folder.

## Slide 250: Schema Name Validator
Impacts
You must update any custom code such as shared content or reports so that they use the truncated part class, custom interface, and attribute names.
You must update the changed names in the code for custom symbols, if they are used.
You must update all data files (such as Excel workbooks) so that they use the new names. The names in GUIDs sheets must be replaced to ensure that the GUID values associated with the old and new names are identical. You must update the GUID sheets to avoid errors in future bulk loads.
After Updating
Update all data files, reports, and shared content code with the truncated names.
Regenerate views on all of the model databases.
Run Synchronize model with catalog with the Regenerate views option selected on all of the projects. Regenerate the reports database for each model database.

## Slide 251: Schema Name Validator

## Slide 252: Adding User Defined Attribute To S3D Database

## Slide 253: Adding User Defined Attribute to S3D Objects
A typical project requirement can be to have a common user attribute to S3D objects. This attribute needs to be bulkloaded into the S3D catalog.

## Slide 254: Adding Approval Status In S3D

## Slide 255: Adding Approval Status in S3D
Project administrators would like to add new approval reasons for S3D objects. These could be bulkloaded to the catalog using a codelist.

## Slide 256: Setup and Administration Lab
Lab 38 - 39

## Slide 257: Model Version Upgrade

## Slide 258: Database Version Upgrade: Overview
Database upgrades are required whenever there is a major change of software version
Smart 3D 2016 supports upgrade from following versions:
  - 2014
  - 2014 R1
It is only possible to upgrade a model configuration using the same database type (Oracle to Oracle or SQL to SQL).

## Slide 259: Database Version Upgrade : Prepare for the Upgrade
Backup all databases and symbols
Verify integrity of data
  Verify/clean specifications
  Synchronize model with catalog
  Resolve To-Do list
  Verify access to reference files
  Run database integrity and clean corrupted elements
Final backup with old version
Prepare the workstation and servers for the upgrade. Make sure all previous versions of Smart 3D are uninstalled and install prerequisites for V2016.

## Slide 260: Database Version Upgrade : Performing the Upgrade
Upgrade your files in the SharedContent share
Manage custom symbols, naming rules and report template files (if necessary)
Restore Site database and upgrade through Database Wizard.
Restore Catalog and Model databases and upgrade through Project Management
Synchronize the Model with the Catalog
Run database integrity and correct possible issues
Regenerate the Reports database
Upgrade Reference Data

## Slide 261: Upgrade SharedContent Wizard
The Upgrade Shared Content wizard will copy your original 2014 or 2014 R1 SharedContent to a new location and then apply appropriate new files from the delivered 2016 SharedContent.
Located on Smart Support under: View Downloads > Smart 3D > Freeware Tools and Utilities > Certified Tools.
The upgrade to the SharedContent must be done BEFORE upgrading the databases to V2016.

## Slide 262: Upgrade SharedContent Wizard

## Slide 263: Upgrade SharedContent Wizard

## Slide 264: Upgrade SharedContent Wizard

## Slide 265: Upgrade SharedContent Wizard

## Slide 266: Upgrade Version – Database Wizard
Upgrade the Site Database (after restoring)

## Slide 267: Upgrade Version Command – Project Management

## Slide 268: Upgrade Version Command – Project Management

## Slide 269: Upgrade Version Command – Project Management

## Slide 270: Upgrade Version Command – Project Management

## Slide 271: Smart 3D Automation Toolkit

## Slide 272: Smart 3D Automation Toolkit
Tool is available on Intergraph® Smart Support site (Previously known as eCustomer site)
Tutorial and Videos are available to download on the same site
Installation is easy and is compatible with all Smart 3D versions
Toolbar can be accessed by tapping Shift key thrice (Shift-Shift-Shift)

## Slide 273: Smart 3D Automation Toolkit
Commands used for administrative workflows:
Select Set browser
Export styles, Style Rules and filters
Import styles, Style Rules and filters
- Filter options